Main Features:

- Dull WM8740 +CS8416 +TAS1020B

- Takes USB input (up to 24Bit/96kHz), optical and coaxial inputs (up to 24Bit/192kHz)

- -110dB SN and -101dB Crosstalk

- Separated battery power supplies for analog section and digital section

- Low pass filter rollable.

- 4-layer gold plated PCB, with high grade components

- Provide Balanced and Unbalanced line out

Contents:

iBassoDB2, power adapter, leather pouch, optical cable, USB cable, 3.5 to 3.5 interconnect, rubber feet, and two extra OPAMPs (LPF).

Caution:

To protect your hearing, please follow the operation guide and do not listen at extremely high volume levels. Extended high volume listening can lead to permanent hearing loss.

Since there are some very sensitive chips on the bottom of the PCB, please always ground yourself, or make sure you are in a static free environment when you open the DB2 case for OPAMP rolling or other modifications.,

Charging the Batteries:

Use the furnished AC adapter or USB cable to charge the batteries. Connect the adapter to the DB2 and turn the charge switch to ON position.

The lamp 1 is the charging indicator for the battery of analog section. The lamp 2 is the charging indicator for the battery of digital section. When the DB2 starts charging, the red color charge lamps turn on. It takes about 7 hours to charge the completely drained batteries. At the point the red color charge lamps turn off, the batteries are fully charged. The DB2 has overcharge protection; you can leave the DB2 plugged and no over-charging concerns.

Warranty:

iBasso DB2 (excluding the accessories and OPAMPs) to be free from malfunctions and defects in both materials and workmanship for one year from the date of purchase. Buyer should retain the warranty card. The warranty card will be required with any request for warranty repair.

This warranty does not apply when failure is due to, accident alteration, water infiltration, modification, unauthorized service, misuse, abuse, use with incompatible accessories or attachments, failure to follow operations, or claim made after the duration of this warranty.

Specifications:

Power Source：Two built-in 4.2V Li-polymer batteries or external power supply

Frequency Response: 10Hz~20 KHz +/-0.5dB

Signal to Noise Ratio：-110dB

Crosstalk: -100dB

Total Harmonic Distortion: 0.009%@1kHz/0dB

Balanced Output Level：2V rms

Unbalanced Output Level：1V rms

Battery Life: Up to 13.5 Hours (when playing 16Bit/44.1kHz)

Battery Charge Time: 7 Hours

External Power supply: 5V DC

Case dimension: 2.2W x 3.9L x 0.95H (inch)

55W x 100L x 24H (mm)

Weight: 171g or 6oz